## Slide 1: From RDMA to SmartNIC
Computer System Principle (2022 Fall)
Xingda Wei
IPADS, Shanghai Jiao Tong University
https://www.sjtu.edu.cn
Credits: Jinwei Xu@IPADS

## Slide 2: Networking is a key component in distributed systems
File server
File:
image
File server
File:
image
File server
File:
image
…
Distributed file system
Database server
Database
user, price
Database server
Database
user, price
…
Distributed database
Caching
Caching server
Caching
Caching server
Caching
Caching server
…
Distributed caching
Load
Balance
Application #1
generate the page
Application server
Application #2
add the order
Application server
…
Internet
…
Users
CDN
Message queue
Example: large-scale websites
  How each component communicates? Networking!

## Slide 3: Review: traditional networking
OSI
  The open systems interconnection (OSI) model
  7-layer architecture

## Slide 4: Review: traditional packet processing in Linux
User space
Kernel space
Network card
  TX/RX queues
  Ring Buffer
  Driver
  TCP/IP
  Socket
  Application
  read(), write()

## Slide 5: Review: Packet processing with DPDK
User space
Kernel space
Network card
  TX/RX queues
  Ring Buffer
  Application
  DPDK

## Slide 6: RDMA: offload the complete network stack to the NIC
RDMA = Remote Direct Memory Access
Direct memory-to-memory data communication over network.

## Slide 7: Review: High-level concepts of RDMA
Queue Pairs (Send Queue, Complete Queue and Receive Queue)
  SQ, CQ & RQ
  A group of queues form an RDMA connection
    Analog to connections in TCP/IP
User posts networking requests to the SQ
  Two-sided: message datagram (like send/recv)
  One-sided: remote read/write (will be talked about later)
Get the completion events of the send requests from the CQ
Receive two-sided messages from the RQ

## Slide 8
Building high-performance distributed systems w/ RDMA

## Slide 9: Case study: distributed in-memory key-value store (KVS)
Key building blocks in distributed systems
  E.g., serve as caching
Provide basic PAI for:
  Get(K) -> V,
  Scan(K,N)
  Update(K,V)
  Insert(K,V)
  Delete(K,V)
Database server
Database
user, price
Application
generate the web page
Application server
File:
image
File server
Local area network
Caching
Caching server
Caching
Caching server
  Not always needed.
  Not the focus of this lecture.

## Slide 10: What is the bottleneck of the such a KV?
…
Memached client
Memached client
Memached client
Memached client
Memached client
Memached client
RDMA
Memached server
A network packet is typically passed through multiple devices
  NIC, switch, PCIe, memory

## Slide 11: What is the bottleneck of the such a KV?
Assumption
  Network card: 100Gbps
  Switch: 100Gbps per port
  PCIe: PCIe 3.0 X 16 = 128Gbps
  Memory bus bandwidth: >= 800Gbps
Clients
Switch
Server
DRAM
Bus
PCIe

## Slide 12: What is the limit of a single core for KVS?
000
x
◉
000
152
x
◉
153
x
John Smith
123-456
◉
Yubin Xia
123-456
x
Xingda Wei
123-456
Poll the request
Find the value of the key
Xingda Wei
keys
Hash
function
Essential operations:
  Poll the request
  Memory accesses to find the value of the key
  Send back the results

## Slide 13: What is the limit of a single core for KVS?
000
x
◉
000
152
x
◉
153
x
John Smith
123-456
◉
Yubin Xia
123-456
x
Xingda Wei
123-456
Poll the request
Find the value of the key
Xingda Wei
keys
Hash
function
Poll request & read request: 100ns
Compute the hash function: 1ns
Read hash table: 200-400ns (depends on the length of the list)
Copy the value: 100ns
Send the reply: 200-800ns
  Using MMIO
600-1400ns!

## Slide 14: Single-core limit of two-sided-based RDMA KVS
1 second = 1000,000,000ns
Assume an average 1000ns per KV request
  One CPU core can only achieve 1 million requests per-second
A high-end server may only have 10-20 CPU cores
  Far gap between CPU & NIC (100 millions)
    Even on a single workload: distributed key-value store

## Slide 15
Summary: CPU can become the bottleneck of in-memory key-value stores

## Slide 16
Note: not a hard conclusion!
Different hardware may yield different performance

## Slide 17: Opportunity: using one-sided RDMA
One-sided RDMA
  READ
    The NIC can directly read the server memory bypassing server CPU
  WRITE
    The NIC can directly write the server memory bypassing server CPU
  ATOMICS (fetch & add, compare & swap)
    The NIC can directly execute atomic operations bypassing server CPU
Bypass the CPU bottleneck !

## Slide 18: One-sided RDMA-based KVS approach
Basic idea:
  Use RDMA READ/WRITE to operate the remote memory like it is local
One-sided RDMA is extremely fast
  E.g., a high-end ConnectX-6 NIC (200Gbps) can process
  100M 64B READs /sec

## Slide 19: One-sided RDMA-based KVS approach: Get(K)
Client
Server
buckets
entries
000
x
◉
000
152
x
◉
153
x
John Smith
123-456
◉
Yubin Xia
123-456
x
Xingda Wei
123-456
Xingda Wei
keys
Hash function
One-sided RDMA:
READ (153)
◉
One-sided RDMA:
READ (bucket)
◉
Yubin Xia
One-sided RDMA:
READ (bucket)
x
Xingda Wei
One-sided RDMA:
READ (value)
123-456

## Slide 20: Challenge: network amplification
Client
Xingda Wei
keys
Hash function
One-sided RDMA:
READ (153)
◉
One-sided RDMA:
READ (bucket)
◉
Yubin Xia
One-sided RDMA:
READ (bucket)
x
Xingda Wei
One-sided RDMA:
READ (value)
123-456
Question
  How many network RTTs are required for a single KV request?
Problem: Network amplification:
  Transfer larger payloads than required
  Need more network RTTs than required
Notes: 问题：这里有哪些network amplification？

## Slide 21: Challenge: network amplification
Client
Xingda Wei
keys
Hash function
One-sided RDMA:
READ (153)
◉
One-sided RDMA:
READ (bucket)
◉
Yubin Xia
One-sided RDMA:
READ (bucket)
x
Xingda Wei
One-sided RDMA:
READ (value)
123-456
Suppose an RDMA card can support 100M/sec one-sided READs
  4 RTTs will degrade the overall performance to 25M/sec
Further: RDMA’s latency is still much higher than local memory accesses!
  100 ns vs. 2000--4000ns, so the latency may be higher than the CPU solution

## Slide 22: Solution: RDMA-friendly data structures
Traditional linked-list—based hash table essentially faces the problem of many pointer-chasing for KV operations
Question:
  Which data structure can we use to improve the performance of RDMA-based in-memory KVS?
Example solution: Cuckoo hashing!

## Slide 23: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
32
84
Buckets0
Buckets1
value
73
16

## Slide 24: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Get()
  Using two hash functions H0 & H1
  The key must be in Buckets0[H0(key)] or Buckets1[H1(key)]
32
84
Buckets0
Buckets1
value
73
16

## Slide 25: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Get()
  Using two hash functions H0 & H1
  The key must be in Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Get(73)
  Buckets0[H0(73)] = 2
32
84
Buckets0
Buckets1
value
73
?
16

## Slide 26: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Get()
  Using two hash functions H0 & H1
  The key must be in Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Get(73)
  Buckets0[H0(73)] = 2 & Buckets1[H1(k73)] = 1
32
84
Buckets0
Buckets1
value
73
16

## Slide 27: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Put()
  Similar as Get()
    1. find the bucket
    2. update the value
32
84
Buckets0
Buckets1
value
73
What about insert?
16

## Slide 28: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
    Question: what if no available space?
32
84
Buckets0
Buckets1
value
73
16

## Slide 29: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(2)
  Buckets0[H0(2)] = 0 & Buckets1[H1(2)] = 0
32
84
Buckets0
Buckets1
value
73
16

## Slide 30: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(2)
  Buckets0[H0(2)] = 0 & Buckets1[H1(2)] = 0
32
84
Buckets0
Buckets1
value
73
Can we insert here?
16

## Slide 31: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(2)
  Buckets0[H0(2)] = 0 & Buckets1[H1(2)] = 0
  Insert here!
84
Buckets0
Buckets1
value
73
32
2
16

## Slide 32: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(9)
  Buckets0[H0(9)] = 0 & Buckets1[H1(9)] = 0
84
Buckets0
Buckets1
value
73
32
2
16

## Slide 33: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(9)
  Buckets0[H0(9)] = 0 & Buckets1[H1(9)] = 0
84
Buckets0
Buckets1
value
73
32
2
16
Both slots are not empty!

## Slide 34: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(9)
  Buckets0[H0(9)] = 0 & Buckets1[H1(9)] = 0
  Cuckoo hashing will kick others to different place to empty
84
Buckets0
Buckets1
value
73
32
2
16

## Slide 35: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(9)
  Buckets0[H0(9)] = 0 & Buckets1[H1(9)] = 0
  Cuckoo hashing will kick others to different place to empty
    Kick 32 (Buckets0[0]) to another place
    Assume: H1(32) = 2
84
Buckets0
Buckets1
value
73
32
2
16
Can insert 9 here!
9

## Slide 36: Cuckoo hashing
84
Buckets0
Buckets1
73
32
2
16
84
Buckets0
Buckets1
73
32
2
16
84
Buckets0
Buckets1
73
32
2
16
9
Insert(9)
Kick(32)
  Buckets0[H0(9)] = 0
  & Buckets1[H1(9)] = 0
H1(32) = 2
Question: what if H1(32) = 3? (which is taken by 84)

## Slide 37: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(9)
  Buckets0[H0(9)] = 0 & Buckets1[H1(9)] = 0
  Cuckoo hashing will kick others to different place to empty
    Kick 32 (Buckets0[0]) to another place
    Question: what if H1(32) = 2 = 3?
84
Buckets0
Buckets1
value
73
2
16
32

## Slide 38: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(9)
  Buckets0[H0(9)] = 0 & Buckets1[H1(9)] = 0
  Cuckoo hashing will kick others to different place to empty
    Kick 32 (Buckets0[0]) to another place
    Kick 2 (Buckets1[0]) to another place
84
Buckets0
Buckets1
value
73
2
16
9

## Slide 39: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(9)
  Buckets0[H0(9)] = 0 & Buckets1[H1(9)] = 0
  Cuckoo hashing will kick others to different place to empty
    Kick 2 (Buckets1[0]) to another place
    Assume: H0(2) = 2
84
Buckets0
Buckets1
value
73
2
16
32
9

## Slide 40: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
Example: Insert(9)
  Buckets0[H0(9)] = 0 & Buckets1[H1(9)] = 0
  Cuckoo hashing will kick others to different place to empty
    Kick 2 (Buckets1[0]) to another place
    Assume: H0(2) = 2 1 What if that happens?
84
Buckets0
Buckets1
value
73
16
32
2
No available slots!

## Slide 41: Cuckoo hashing
Cuckoo hashing
  Maintain two hash buckets
Insert()
  Much complicated: should insert to Buckets0[H0(key)] or Buckets1[H1(key)]
  If no available slots, rehashing & repeat the above insert process
  Rehashing: enlarge the buckets (typically X2)
Buckets0
Buckets1

## Slide 42: Cuckoo hashing
Cuckoo hashing
  Two tables & Two hash functions (H1, H2)
  The key can only at T1[H2(key)] or T2[H2(key)]
Pros
  Good for read: at most two 2 random I/O for get
Cons
  Insertion is complex and can issue many random disk I/O
  Rehashing is required if there are many insertions, which is extremely slow
    Expanding the table, and re-insert all the keys in the new table (!)
Notes: We will not cover many details

## Slide 43: Cuckoo hashing is an RDMA-friendly data structure
Cuckoo hashing
  Two tables & Two hash functions (H1, H2)
  The key can only at T1[H2(key)] or T2[H2(key)]
Get only needs at most 3RTTs to finish
Much complicated for insertion
  Kicking KV to different buckets upon hash collisions
  We will talk about it later

## Slide 44: Get(K) with cuckoo hashing
Server
buckets
entries
000
000
152
153
John Smith
123-456
Yubin Xia
123-456
Xingda Wei
123-456

## Slide 45: Get(K) with cuckoo hashing
Server
buckets
entries
000
000
152
153
John Smith
123-456
Yubin Xia
123-456
Xingda Wei
123-456
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
123-456
Xingda Wei
One-sided RDMA:
READ (value)

## Slide 46: Drawbacks of Cuckoo hashing
Extra RTTs for lookup in case of hash collision
Observation
  RDMA has similar performance of larger reads as small reads
  Why? Hardware has a fixed granularity for access,
    E.g., PCIe uses 64B
    The NIC processing overhead may dominate for "not so large” messages

## Slide 47: Performance characteristics of RDMA

## Slide 48: Idea: use large buckets to reduce hash collision
Suppose we want to insert key 9
  H0(9) = 0
Normal cuckoo hashing
  Insert to buckets 1
    Meaning another RDMA RTT for Get(9)
Solution: store an overflow slot at each bucket
  Reduce the probability of hash collision
    At the cost of extra space
    At the cost of extra lookup (trivial)
84
Buckets0
Buckets1
73
16
32
84
Buckets0
Buckets1
73
16
32

## Slide 49: Short-summary of RDMA-based data structures
Existing RDMA-based KVS adopt two design decisions
Customized hash data structure
  Pliaf@ATC’13 (Cuckoo hashing)
  FaRM-KV@NSDI’14 (Hopscotch hashing)
Large buckets that suits RDMA
  FaRM-KV uses 6 entries per read
  DrTM-KV@SOSP’15 (cluster chaining, a configurable number of entries per-bucket)

## Slide 50: What about put?
Much complicated than the Get()
  Kicking entries in case of multiple hash collisions
  Re-construct the hash table in case of rehashing
Solution: hybrid approach
  Use RPC for the put operations
  Only use RDMA for get Get()
Observation
  Read-only dominates the real workload [1]
  [1] Tao: Facebook’s distributed data store for the social graph. ATC’13

## Slide 51
Challenge: read/write between different devices

## Slide 52: Running put & get concurrently at different devices
Server CPU
buckets
entries
000
000
152
153
John Smith
123-456
Yubin Xia
123-456
Xingda Wei
123-456
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei

## Slide 53: Running put & get concurrently at different devices
Server CPU
buckets
entries
000
000
152
153
John Smith
123-456
Yubin Xia
123-456
Xingda Wei
123-456
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei
Put(Wei Xingda)
Hash(Wei Xingda) = 153

## Slide 54: Running put & get concurrently at different devices
Server CPU
buckets
entries
000
001
152
153
John Smith
123-456
Yubin Xia
123-456
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei
Put(Wei Xingda, xxx)
Hash(Wei Xingda) = 153
Xingda Wei
123-456

## Slide 55: Running put & get concurrently at different devices
Server CPU
buckets
entries
000
001
152
153
John Smith
123-456
Yubin Xia
123-456
Wei Xingda
xxx
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei
Put(Wei Xingda, xxx)
Hash(Wei Xingda) = 153
Xingda Wei
123-456

## Slide 56: Running put & get concurrently at different devices
Server CPU
buckets
entries
000
001
152
153
John Smith
123-456
Yubin Xia
123-456
Wei Xingda
xxx
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei
Put(Wei Xingda, xxx)
Hash(Wei Xingda) = 153
Xingda Wei
123-456
xxx
One-sided RDMA:
READ (value)
Inconsistent!

## Slide 57: Tradition solution #1: locking?
The simplest solution: spinlock
uint64_t lock = 0;
fn lock_cpu() {
while True {
if CPU_CAS(&mut lock, 0, 1) {
return;
}
}
}
uint64_t addr = 0; // &lock
fn lock_cpu() {
while True {
if RDMA_CAS(addr, 0, 1) {
return;
}
}
}

## Slide 58: Problem #1: Extra roundtrips
Client
RDMA
CAS
RDMA
WRITE
Lock
Xingda Wei
123-456
Read bucket
Read value
Unlock

## Slide 59: Problem #2: ATOMIC issues between RDMA & CPU
RDMA & CPU uses different atomic implementations
  NIC & CPU uses separate locking to ensure atomicity (on its perspective)
  NIC: acquire the NIC’s internal lock for atomics
  CPU: lock the memory bus for atomics
Thus, RDMA CAS may misses the updates of a CPU CAS!

## Slide 60: Traditional solution #2: lock-free read?
Basic idea (similar to OCC)
  First read without protection
  Check to ensure the read content has unchanged
High-level procedure of Insert upon modifying a bucket
  Lock the bucket
  Do the insertion
  Increase the version
  Unlock the bucket
Yubin Xia
123-456
Bucket
1
Version
Key
Value
Lock

## Slide 61: Traditional solution #2: lock-free read?
High-level procedure of READ
  Read the bucket version & key & lock (assume atomic)
    Retry if the lock is held
  Read the bucket value
  Re-read the bucket version and lock
  Retry (1) if the version doesn’t match or lock is held
Yubin Xia
123-456
Bucket
1
Version
Key
Value
Lock
Similar to the validation in OCC

## Slide 62: Lock-free READ in RDMA-based KVS
Server CPU
buckets
entries
000
001
152
153
John Smith
123-456
Yubin Xia
123-456
Xingda Wei
123-456
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei
xxx
1
1
1
1
1

## Slide 63: Lock-free READ in RDMA-based KVS
Server CPU
buckets
entries
000
001
152
153
John Smith
123-456
Yubin Xia
123-456
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei
xxx
1
1
1
2
1
Put(Wei Xingda, xxx)
Hash(Wei Xingda) = 153
Wei Xingda
xxx
Xingda Wei
123-456

## Slide 64: Lock-free READ in RDMA-based KVS
Server CPU
buckets
entries
000
001
152
153
John Smith
123-456
Yubin Xia
123-456
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei
xxx
1
1
1
2
1
Put(Wei Xingda, xxx)
Hash(Wei Xingda) = 153
Wei Xingda
xxx
Xingda Wei
123-456
One-sided RDMA:
READ (153)

## Slide 65: Lock-free READ in RDMA-based KVS
Server CPU
buckets
entries
000
001
152
153
John Smith
123-456
Yubin Xia
123-456
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei
xxx
1
1
1
2
1
Put(Wei Xingda, xxx)
Hash(Wei Xingda) = 153
Wei Xingda
xxx
Xingda Wei
123-456
One-sided RDMA:
READ (153)
One-sided RDMA:
READ (153)
2
Retry…

## Slide 66: Problem still: Extra roundtrips
Client
Xingda Wei
keys
Hash function 0
One-sided RDMA:
READ (153)
Xingda Wei
xxx
1
One-sided RDMA:
READ (153)
One-sided RDMA:
READ (153)
2
Retry…
Single-machine solution not fit well

## Slide 67: Self-verify data structure
Goal: detect incorrect data structure accesses due to read/write races
  Without issuing more network RTTs
    E.g., lock or read validations
Idea:
  Use some kind of checksum to ensure the integrity of the data
    i.e., the value belong to the value
Yubin Xia
123-456
Bucket
Key
Value
Lock
C
Checksum

## Slide 68: Not an ending story
The story of RDMA-friendly data structure is not an end
  Currently, we only show hash-table-based design
  What about B+Tree? An open problem to discover
RDMA is also not an end
  One-sided primitives, though simple, has been proved powerful
  What about more powerful primitives?
    E.g., SmartNICs

## Slide 69
Understanding the implementation details of RDMA matters

## Slide 70: One-sided RDMA primitive seems simple
The network card can read/write server memory
  Is that simple?

## Slide 71: Life cycle of an RDMA one-sided WRITE
[1] Memory-mapped IO

## Slide 72: Life cycle of an RDMA one-sided WRITE
Why efficient?
[1] Memory-mapped IO

## Slide 73: What are the costs in a one-sided WRITE?
The network latency is still high!
  At least 1us
  Hard to hide due to hardware, network delay, etc.
Suppose we post RDMA requests in a synchronous way
  A single core can only achieve 1M reqs/sec
  On the other hand, RDMA can achieve 10-100M reqs/sec!

## Slide 74: How to avoid waiting? Add more concurrency
Outstanding request & coroutine
  Outstanding requests means keep multiple RDMA requests on-the-fly
  Coroutine is the same as traditional asynchronous I/O programming
    Yield after posting a request
Goal:
  Hide polling latency

## Slide 75: Other costs: MMIO
There are several ways to keep multiple requests on-flight
  The common way is to use one MMIO per request
MMIO is (relatively) costly
  400 ~ 1000 cycles

## Slide 76: Optimization: doorbell batching
Credits: Anuj Kalia
There are several ways to keep multiple requests on-flight
  The common way is to use one MMIO per request
MMIO is (relatively) costly
  400 ~ 1000 cycles
Doorbell batching:
  one MMIO to post a batch of requests, NIC uses
  DMA to read them

## Slide 77: Effects of optimizations
Multiple 64-byte object read micro-benchmark
  Passive Ack (PA): omit the ack of the request
Throughput (millon reqs/second)

## Slide 78
More about RDMA details

## Slide 79: More about RDMA details

## Slide 83: RDMA: out memory design
Connection, translation, permissions, etc. information are stored on the host memory
  NIC only caches them in its SRAM
  However, NIC has limited SRAM!
    Even high-end NIC today has 2MB buffer (ConnectX-5)

## Slide 84: RDMA: out memory design
Connection, translation, permissions, etc. information are stored on the host memory
  NIC only caches them in its SRAM
  However, NIC has limited SRAM!
    Even high-end NIC today has 2MB buffer (ConnectX-5)
What if the NIC cache misses?
  Use PCIe read to fetch them

## Slide 85: RDMA: out memory design
Connection, translation, permissions, etc. information are stored on the host memory
  NIC only caches them in its SRAM
  However, NIC has limited SRAM!
    Even high-end NIC today has 2MB buffer (ConnectX-5)
What if the NIC cache misses?
  Use PCIe read to fetch them
  Compete DMA w/ normal requests!

## Slide 87: RDMA: out memory design makes cache miss costly
Driver stores these at the host memory
  NIC caches a portion of such information
Fetch miss items using PCIe read
  ~ 1us additional latency, fetch from DRAM using PCIe read
  For comparison, RDMA one-sided read takes ~2us

## Slide 88: Some can be mitigated, some can not
FaRM@NSDI’14 uses huge page (2MB page instead of 4KB page)
  Reduce #PTE entries
  E.g., 1GB memory only requires 2048 PTE entries, while 4KB needs 250,000 entries

## Slide 89: Some can be mitigated, some can not
LITE@SOSP’17 takes to another extreme; it directly physical memory, and uses kernel for security check
  No PTE and keys need to be cached at the NIC!

## Slide 90: But connection information still cannot avoid
NIC must cache the connection information to accelerate the process
  What if there is a cache miss?

## Slide 91: But connection information still cannot avoid
NIC must cache the connection information to accelerate the process
  What if there is a cache miss?
Performance drop caused by cache misses
  Extra PCIe READ for each request
    1 -> 2
[1] credits: eRPC@NSDI’19

## Slide 92
This leads to another extreme

## Slide 93: Case study: FaSST@OSDI16
RDMA provides an unreliable transport: unreliable datagram (UD)
  Similar to UDP (consider traditional RDMA connection as TCP)
UD is scalable:
  No connection information is kept at the NIC
Drawbacks of UD:
  No reliability guarantee
  Only supports two-sided RDMA
Two-sided RDMA is sufficient for RPC: a key building block in distributed systems!

## Slide 94: Case study: FaSST@OSDI16
RDMA provides an unreliable transport: unreliable datagram (UD)
  Similar to UDP (consider traditional RDMA connection as TCP)
UD is scalable:
  No connection information is kept at the NIC
Drawbacks of UD:
  No reliability guarantee
  Only supports two-sided RDMA
Two-sided RDMA is sufficient for RPC: a key building block in distributed systems!

## Slide 95: Does no reliability a significant problem?
RDMA provides an unreliable transport: unreliable datagram (UD)
  Similar to UDP (consider traditional RDMA connection as TCP)
UD is scalable:
  No connection information is kept at the NIC
Drawbacks of UD:
  No reliability guarantee
  Only supports two-sided RDMA

## Slide 96: Not that significant: RDMA rarely drop packets
#1. RDMA requires the link-layer to guarantee reliability
  e.g., RoCE uses packet flow control to avoid switch drop packets
#2. The semantic of RPC simplifies the packet drop checking
  The remote end must send a reply
  If timeout, treat the packet as loss

## Slide 97: Other benefits of using RPC
Reduced network roundtrips
  Compared to one-sided RDMA
  Example: implement a key-value store using FaRM’s approach

## Slide 98: Takeaway of RPC vs. one-sided RDMA
Not a hard conclusion!
Pros of one-sided
  Energy efficient
  Better (theoretical performance)
  CPU bypassing
Cons of one-sided
  Poor offloading semantic
  Scalability issues
Not a hard conclusion!
Pros of two-sided
  Easy programming
  Scalable performance
Cons of two-sided
  Low performance when scalability is not an issue
  CPU overhead

## Slide 99: Trends of scalability of one-sided RDMA
New NICS are more scalable!
  Partly not due to the increased SRAM
  But a better cache management, NIC pipeline processing, increased PCIe bandwidth etc.
Example:
  Connect-X5 (2017) scales to 80 all-to-all mappings[1,2], while Connect-X3 (2014) only scales to a few
Advanced RDMA transport:
  Dynamic connect transport allows one QP to connect to different nodes

## Slide 100
But the limited offloading semantic of RNIC is still a problem.

## Slide 101: RDMA: limited functionalities
One-sided RDMA only supports simple READ/WRITE semantics
  Distributed systems typically are more complex
  Example: lookup in a key-value store still requires multiple one-sided roundtrips

## Slide 102
Can RNIC do better?

## Slide 103: Being smart with SmartNICs

## Slide 104: Overview of design space of SmartNIC
Provide more flexible (programmable) semantic on the NIC
What is the accelerator?
  RDMA: ASIC -- only read/write
  SmartNIC: FPGA, Arm SOC, MIPS, etc.
What is the programming abstraction?
  Verbs (RDMA), C/C++, P4, etc.
Where to place the accelerator?
  on-path vs. off-path

## Slide 105: Overview of design space of SmartNIC
SmartNIC can have various computing units
  Trade-off between performance & flexibility

## Slide 106: On-path vs. off-path for intercepting networking requests
Pros
  Lower latency
Cons
  No resource isolations
Pros
  Clear resource isolation
Cons
  Latencies added due to NIC switch

## Slide 107: RDMA NICs can also be programmable

## Slide 108: SmartNIC in 1990s: Support Innovation
Which Functions Belong to NICs? Which protocols are better?
  The network protocols are evolving quickly (e.g., ATM or Ethernet? )
  People use SmartNICs to evaluate different protocols quickly
Notes: ATM: a network protocol
90年代的智能网卡是作为实验平台来使用的。当时的网络界百花齐放，有许多问题悬而未决。所以有一个可编程的网络设备可以方便地进行开发和实验。而到了2000年以后，很多问题得到了结果，以太网一统江湖。这个时候固化的网卡就占了上风

## Slide 109: SmartNIC in 2010s+: Software-Defined Offloading
Networking Become Dynamic
  Software-Defined Networking
  Network virtualization
Heterogeneous Computation
  Multicore CPU hits the Power Wall
  Domain specific, higher performance (e.g., RDMA-enabled KVS)

## Slide 110: SmartNIC in 2010s+: Software-Defined Offloading
Host
NIC
Ethernet
VM/Container
Physical
SR-IOV
KV-Store
DFS
NVMe-oF
VM
VM
CPU
FPGA
TCP/IP
VirtIO-blk
Hashing
Dedup.
Comp.
RoCE
IPsec
Encrypt.
RAND
OVS
DPDK
SDN
OVS

## Slide 111: Challenges in offloading
Costly communications between host and SmartNIC
  The latency of PCIe is much higher than DRAM access
    E.g., 1000ns vs. 100ns
Wimpy computing power due to energy restrictions
  NIC’s on-board CPU is typically slower than the host

## Slide 112: Brief summary of SmartNICs
Note that each type of the NIC can be on-path or off-path
 | Product | Programmable Unit | Programming Language | Performance | Flexibility | Cost
ASIC Based | Mellanox ConnectX-6 | \ | \ | High | Low | Low
FPGA Based | Xilinx U25 | FPGA | Hardware description language | Medium | High | High
SoC Based | Mellanox BlueField | Multicore Processor | Any | Low | Very high | Medium

## Slide 113
An overview of SmartNIC performance

## Slide 114: Deconstructing SmartNICs
Traffic control
Computing units
Onboard memory
Host communication
Traffic manager /
NIC switch
TX/RX ports
DMA engine
Multicore processor
NIC core
L1 Cache
Accelerator
Packet processing
Domain specific
Packet buffer
Scratchpad
L2/DRAM
DMA engine
Multi-queue
FPGA

## Slide 115: Structural Difference between on-path & off-path NICs
NIC switch
NIC cores
TX/RX ports
Host cores
Off-path SmartNIC
Traffic
Traffic manager
NIC cores
TX/RX ports
Host cores
On-path SmartNIC
Traffic
Firmware
Full OS
10GbE LiquidIOII CN2350, 1.2GHz
25GbE Stingray PS225, 3.0GHz

## Slide 116: Packet Processing Performance
SmartNIC architecture collects taxes for the offloading power
  What are the detailed costs?
Microbenchmark
  Forwarding without any additional processing
  Quantifies the default forwarding tax of SmartNICs
10GbE LiquidIOII CN2350, 1.2GHz
25GbE Stingray PS225, 3.0GHz
Notes: Echo server

## Slide 117: Processing Headroom
Using the same microbenchmark, except
  Forwarding throughput as we introduce additional per-packet processing
  Headroom is workload dependent and only allows for the execution of tiny tasks
Insights
  Network incurs non-trivial tax on SmartNIC, and the request payload matters

## Slide 118: On-board DRAM
Like traditional server, SmartNIC also has memory hierarchy
  L1 cache
  Packet buffer
  L2 cache
  NIC local DRAM
Insight: avoid cache misses on SmartNICs
Notes: 就是working-set超过cache size的话，性能影响会很大，因为DRAM访问延迟高，而网卡的L2和host的L3差不多

## Slide 119: Host communication performance
Two ways
  DMA over PCIe
    Blocking
    Non-blocking
  RDMA Primitives (2X+ latency)
Insight
  RDMA simplifies programming but at the cost of performance
DMA Latency on the 10GbE LiquidIO CN 2350
RDMA Latency on the 25GbE BlueField 1M332A

## Slide 120: Brief Summury of on-path vs. off-path
 | On-path | Off-path
Programming interface | Low-level: RX/TX queue, packet buffer management, DMA engine, et. al; | Full Linux OS
How to offload | Add logic in the packet processing pipeline | Direct traffic to cores
Access host memory | PCIe DMA | RDMA
Limitation | Host traffic consume NIC cores | Higher latency to host memory

## Slide 121
Case study: KV-Direct@SOSP’17

## Slide 122: Key-Value Store in Data Centers
Web Cache
Shared Data Structure
Key Value
User ID Recent Tweets
SQL Query result
Session Browser cookies
Key Value
Graph node List of edges
Feature Weight
Shard Sequence number

## Slide 123: Key-Value Store in Data Centers
Shared Data Structure
Key Value
Graph node List of edges
Feature Weight
Shard Sequence number
Design Goals
High throughput
Low tail latency
Write intensive
Vector operations
Atomic operations

## Slide 124: Key-Value Store Architectures
Software (Kernel TCP/IP)
Bottleneck: Network stack in OS
(~300 Kops per core)
Software (Kernel Bypass)
e.g. DPDK, mtcp, libvma, two-sided RDMA
Bottleneck: CPU random memory access and KV operation computation
(~5 Mops per core)
One-sided RDMA
Communication overhead: multiple round-trips per KV operation (fetch index, data)
Synchronization overhead: write operations

## Slide 125: Key-Value Store Architectures
KV-Direct FPGA + NIC
Offload KV processing on CPU to Programmable NIC

## Slide 126: KV-Direct Architecture

## Slide 127: Performance Challenges
(Intel Stratix V)
Notes: First, PCIe credit-based flow control constrains the number of in-flight requests for each DMA type.
Second, DMA read requires assigning a unique PCIe tag to identify DMA responses which may come out of order. The DMA engine in our FPGA only support 64 PCIe tags, further limiting our DMA read concurrency to 64 requests, which renders a throughput of 60 Mops.

## Slide 128: Performance Challenges
13 GB/s
120 Mops
Header overhead and limited parallelism
Be frugal on memory accesses
Notes: First, PCIe credit-based flow control constrains the number of in-flight requests for each DMA type.
Second, DMA read requires assigning a unique PCIe tag to identify DMA responses which may come out of order. The DMA engine in our FPGA only support 64 PCIe tags, further limiting our DMA read concurrency to 64 requests, which renders a throughput of 60 Mops.

## Slide 129: Performance Challenges
1us delay
120 Mops
Atomic operations have dependency:
PCIe latency hiding

## Slide 130: Performance Challenges
1us delay
120 Mops
Load dispatch
0.2us delay
100 Mops

## Slide 131: Performance Challenges
1us delay
120 Mops
Client-side batching
Vector-type operation
0.2us delay
100 Mops
60 Mops

## Slide 132: Design Principles
Minimize DMA requests per KV operation
Hide PCIe latency
Leverage throughput of both on-board and host memory
Offload simple client computation to server

## Slide 133: Minimize DMA requests per KV operation
Hash table: minimal access per GET & PUT
  Cuckoo hashing : constant GET, sacrifice PUT
  Log-structured memory: fast PUT, sacrifice GET
  KV-Direct: Bucketized chaining: Close to 1 per GET, 2 per PUT

## Slide 134: Minimize DMA requests per KV operation
Slab memory allocator
  Main logic runs on the host
  Cache free slab pool on the NIC
  0.07 amortized DMA operations per (de)allocation

## Slide 135: Hide PCIe Latency
Memory Dependency

## Slide 136: Hide PCIe Latency
Reservation Station
  Cache latest values

## Slide 137: Hide PCIe Latency
Pipeline Stall

## Slide 138: Hide PCIe Latency
Reservation Station
  Cache latest values
  Track inflight ops and their execution context

## Slide 139: Hide PCIe Latency
Out-of-order Execution
  191x single-key atomics, 20x long-tail workload

## Slide 140: Leverage Throughput of Both Memory

## Slide 141: Leverage Throughput of Both Memory
Load Dispatch = Cache + Load Balance

## Slide 142: Evaluation

## Slide 143
Detailed performance analysis of a SmartNIC

## Slide 144: From RNIC SmartNIC: larger offloading design spaces
Host DRAM
Host DRAM
NIC cores
Network
One-sided
Two-sided
The central processing unit RDMA-capable NIC (RNIC) are NIC cores
  ASIC that implements one-sided and two-sided operations (not programmable)
SmartNIC extends RNIC to support programmable capabilities
NIC cores
Network
One-sided
Two-sided
SoC cores & mem
DRAM
App-specific
computation
Notes: The limitation of RDMA is that its offloading options are restricted by the NIC ASIC cores.In response to this, modern NICs are extending the RDMA NIC to equip with programmable computing units, such as SoC cores. These units enable developers to offload more complex application logic onto the NIC.

## Slide 145: From one-sided RDMA to SmartNIC, does it help?
SmartNIC: RNIC equip with a programmable SoC (RNIC + SoC)
Back to our initial case study: Get(K) -> V in key-value storage
  We can use the programmability of SmartNIC to execute the Get() w/o amplification
Client
RNIC
Server
Host DRAM
RNIC
Index
Values
Index
Get(K)
V
RDMA
READ
RDMA
READ
Index
Values
Client
RNIC
Server
Host DRAM
RNIC
Index
Get(K)
V
SoC
V
SEND
RECV
Notes: With the help of SoC, it is possible to offload the more complex KVS logic to the NIC, addressing the network amplification problem of one-sided RDMA, while avoid the CPU bottleneck of the two-sided RDMA (click).
Specifically, we can send the request to the SmartNIC SoC to help execute the request.
.

## Slide 146: From one-sided RDMA to SmartNIC, does it help?
Our (naïve) SmartNIC-KVS is 14% of the RDMA-KVS !! (workload: YCSB-C (100% Get))
  RDMA-KVS: DrTM-KV [SOSP’15]
  SmartNIC-KVS: leverage SEND/RECV to offload Get to the NIC SoC
Index
Values
Client
RNIC
Server
Host DRAM
RNIC
Index
Get(K)
V
SoC
V
SEND
RECV
Chart: Throughput (Mreqs/sec)
| Throughput: Mops
RDMA-KVS | 53.8
SmartNIC-KVS | 5.1
DrTM-KV
SmartNIC-KV
Notes: However, our initial results show that when we offload the request to the SoC, SmartNIC-accelerated KVS can only achieve 14% of the performance of RDMA-accelerated KVS.
The problem can be the weak computation power of SoC or the hidden performance tax introduced by the SmartNIC hardware.

## Slide 147: SmartNIC is more complex than we have thought
Many SmartNIC architectures exist (More complex than we thought)
We focus on off-path SmartNIC, a widely used SmartNIC architecture
  Representative example: NVIDIA Bluefield-2 SmartNIC
NIC cores
SoC cores & mem
DRAM
Host DRAM
NIC cores
SoC cores & mem
PCIe1
PCIe0
PCIe
Switch
DRAM
Cache
Host DRAM
Cache
Discovered via exp + doc
Notes: By examining the usually incomplete documentation of SmartNICs and conducting extensive evaluations (click), we discovered that the hardware units of SmartNICs are much more complex than we had previously thought. If developers do not carefully consider these factors, they may encounter unexpected performance anomalies.
Specifically, the SmartNIC doesn't simply add the SoC to it. The SoC is bridged with the NIC ASIC cores with a PCIe switch, where there are two PCIe channels linked the NIC cores and switch and the switch with the host together. Meanwhile, the SoC itself is also complex, with memory hierarchies and some accelerators.
Note that the study primarily focus on the off-path SmartNIC.

## Slide 148: Our work: the most comprehensive characterization on SmartNIC
Existing studies exist[1][2][3], which provides valuable insights
  The mostly focus on the offloading computation power of the SmartNIC
  A known takeaway is that: SmartNIC’s SoC cores are wimpier than the host
[1] Offloading distributed applications onto smartnics using ipipe. SIGCOMM’19
[2] Performance characteristics of the bluefield-2 smartnic, arXiv
[3] A dbms-centric evaluation of bluefield dpus on fast networks. ADMS’22
148
Cache
DRAM
 | L1 | L2 | L3 | DRAM
SoC | 4x | 4x | N/A | 2x
Host | 1x | 1x | 1x | 1x
Benchmark | SoC | Host
Multi-core Coremark | 0.2x | 1x
Single-core Coremark | 0.5x | 1x
DPDK hash_perf | 0.3x | 1x
DPDK readwrite_lf_perf | 0.3x | 1x
Memory access speed [1] (lower is better)
CPU scores[1] (higher is better)
Focus of existing work
Notes: There have been valuable measurement studies in the literature that analyze the performance characteristics of SmartNICs. Most of them focus on the SmartNIC's programmable computing capabilities.
A well-known finding is that the computing capability of SmartNICs is weak except for the limited accelerators. This observation is unlikely to change due to the power constraints of the NIC. Therefore, we take the weak computing power of SoC as a premise of our study.

## Slide 149: Our work: the most comprehensive characterization on SmartNIC
An important (and basic) component of NIC: communication, is not well explored
  The communication paths of SmartNIC are more complex than other NICs
Network
Traditional NICs (RDMA or non-RDMA)
Path #1: Client → NIC → Host memory
Notes: However, the communication performance features of SmartNIC have not been well-explored, which is actually an essential functionality of a network device. So understanding them is definitely important.
The communication path of SmartNIC is much more complex than traditional NICs. Specifically, traditional NICs only provide a single communication path to the system, which connects the network traffic to the host CPU and vice versa.

## Slide 150: Our work: the most comprehensive characterization on SmartNIC
An important (and basic) component of NIC: communication, is not well explored
  The communication paths of SmartNIC are more complex than other NICs
SmartNIC
Network
Path #1: Client → NIC → Host memory
Notes: SmartNIC also provides this capability.

## Slide 151: Our work: the most comprehensive characterization on SmartNIC
An important (and basic) component of NIC: communication, is not well explored
  The communication paths of SmartNIC are more complex than other NICs
SmartNIC
Path #1: Client → NIC → Host memory
Path #2: Client → NIC → SoC memory
Network
Notes: Meanwhile, SmartNIC enables more paths, including communicating with the on-board SoC memory and cores, (click)

## Slide 152: Our work: the most comprehensive characterization on SmartNIC
An important (and basic) component of NIC: communication, is not well explored
  The communication paths of SmartNIC are more complex than other NICs
SmartNIC
Path #1: Client → NIC → Host memory
Path #2: Client → NIC → SoC memory
Path #3: SoC memory ←→ host memory
Network
Notes: and the SoC can further communicate with the host, and vice versa.

## Slide 153: Our work: the most comprehensive characterization on SmartNIC
An important (and basic) component of NIC: communication, is not well explored
  The communication paths of SmartNIC are more complex than other NICs
SmartNIC
Path #1: Client → NIC → Host memory
Path #2: Client → NIC → SoC memory
Path #3: SoC memory ←→ host memory
Network
Performance characterization on all them!
Notes: Characterizing these paths are the focus of this work.

## Slide 154: What do we characterize ?
SmartNIC hardware implication to the communication performance
Design guideline on building systems with SmartNICs
Notes: More specifically, our characterization aims to answer two specific questions by measuring the performance of off-path SmartNICs:
What is the performance implication of the off-path SmartNIC hardware architecture?
Given these implications, how can system developers better utilize the SmartNIC?

## Slide 155: Finding 1. SmartNIC < RNIC for path #1
Chart: 
| READ | WRITE | SEND/ RECV
RNIC (1) | 2.1 | 2 | 3.1
SNIC (1) | 2.6 | 2.3 | 3.3
SNIC (2) | 0 | 0 | 0
SNIC (3) | 0 | 0 | 0
The path #1 is long on the SmartNIC
  Due to the intervention of PCIe switch
  The one-way switch pass latency (300ns) is non-trivial for microsecond-scale computing
Client
SoC
Host
READ
WRITE
SEND/RECV
Primitives evaluated
WRITE
RNIC vs. SmartNIC
Evaluation setup:
ConnectX-6 (RNIC) vs. Bluefield -2 (SmartNIC)
Both NICs use the same NIC cores
Latency (us)
Payload: 64B
Notes: Our first finding is that extending the RNIC to a SmartNIC will slow down path 1 in terms of latency and throughput.
This is because extra hardware components, i.e., the SmartNIC's internal PCIe and PCIe switch, are added to the critical path of each network packet process.
Our empircial results show that passing them will increase request latency by approximately 300ns. This delay is significant given the low latency of RNIC, which operates on the microsecond scale.

## Slide 156: Finding 2. Path #2 is fast except for S/R
Communication with the SoC is faster except for the SEND/RECV (S/R)
  Due to the reduced PCIe pass (i.e., PCIe0)
  SEND/RECV is bottlenecked by the SoC cores
Client
SoC
Host
READ
WRITE
Primitives evaluated
S/R
WRITE
RNIC vs. SmartNIC
Evaluation setup:
ConnectX-6 (RNIC) vs. Bluefield -2 (SmartNIC)
Both NICs use the same NIC cores
Path #2
Chart: 
| READ | WRITE | SEND/ RECV
RNIC (1) | 2.1 | 2 | 3.1
SNIC (1) | 2.6 | 2.3 | 3.3
SNIC (2) | 2.3 | 2.3 | 4.3
SNIC (3) | 0 | 0 | 0
Latency (us)
Fast interconnect
other than PCIe
Path #1
Payload: 64B
Notes: Compared to Path #1, Path #2 has much better RDMA performance, except for send/recv, which is bottlenecked by the weak SoC computing power.
Path #2 is faster because it omits passing one PCIe channel from the switch to SoC. Specifically, the PCIe switch directly links to the SoC with a faster internal connection other than PCIe, thanks to the close packaging of the hardware.

## Slide 157: Finding 3. Anomalies exist paths involving SoC
Example. Degraded bandwidth (for READ) with large data transfer
  Observation: SoC supports a smaller PCIe MTU than host
  Result: more PCIe packets processed, may cause HoL
Advice: proactively segmented large READ
 | Host | SoC
PCIe MTU | 512B | 128B
Client
SoC
Host
READ
READ
PCIe packets
transferred
Chart: READ payload (Bytes)
| 256KB | 1MB | 9MB | 64MB
SNIC (1) | 191.3 | 191.3 | 190 | 193.3
SNIC (2) | 190 | 191.3 | 184.8 | 103.1
Bandwidth (Gbps)
Suspect meet HoL
Notes: Although Path 2 is faster due to the closer package of SoC and NIC, the weaker hardware of SoC introduces anomalies even to packets not directly processed by the SoC cores.
For example, when issuing large RDMA READs to SoC, we observe a performance collapse on Path 2. We suspect this is due to head-of-line blocking, as more PCIe packets need to be processed at the DMA engine for larger reads.
One may wonder why Path 1 doesn’t suffer from this phenomenon. This is because, due to the more powerful host CPU, Path 1 can support a 4X PCIe MTU compared to SoC. Consequently, Path 1 only requires processing one fourth of the PCIe packets, which is much smaller than Path 2.

## Slide 158: Finding 4. Path #3 has trade-offs
Many alternatives to implement Path #3
  The simplest (& easiest to use one): RDMA
Yet, RDMA needs to pass RNICs & PCIes
  For networking support
Client
SoC
Host
READ
WRITE
SEND/RECV
Primitives evaluated
Chart: 
| READ | WRITE | SEND/ RECV
RNIC (1) | 2.1 | 2 | 3.1
SNIC (1) | 2.6 | 2.3 | 3.3
SNIC (2) | 2.3 | 2.4 | 4.3
SNIC (3) | 3.3 | 2.9 | 4.4
Evaluation setup:
ConnectX-6 (RNIC) vs. Bluefield -2 (SmartNIC)
Both NICs use the same NIC cores
Latency (us)
Higher latency than other paths
Notes: Next, we will explore the performance features of path 3. Interestingly, SmartNIC provides several alternatives for path 3, and each alternative has different trade-offs.
The most straightforward option is to use RDMA to communicate between the host and SoC. However (click), this option has higher latency than the others, even though it doesn't go through the network.
Why? Because to support the RDMA protocol, packets must first come to the NIC core for processing, then be transferred back. The transfer is necessary for network protocol support, but the added cost is non-trivial.

## Slide 159: Finding 4. Path #3 has trade-offs
RDMA, though simple, has two problems for Path #3
  High latency due to additionally passes hardware units
  Bandwidth interference to the others
RDMA of path #3 overuses the PCIe bandwidth
Client
SoC
Host
Client  SoC  Host
Path #2
Path #3
200Gbps
256Gbps
What is the performance of path#2 + path#3?
Case study: file replication in LineFS [SOSP’21]
Notes: To make matters worse, RDMA can overuse the PCIe bandwidth between the PCIe switch and NIC. This occurs because a single unidirectional traffic will occupy the bidirectional bandwidth of PCIe. (click)
What anomaly maybe caused by this fact? Let's consider a typical offloading design, where the client offloads a piece of data to the SoC for processing, and then the SoC sends it out to the host. This design is adopted by the state-of-the-art SmartNIC-accelerated system. (click)
For the targeted application, a system requirement is to saturate the network bandwidth. However,this offloading design fails to do so.

## Slide 160: Finding 4. Path #3 has trade-offs
RDMA, though simple, has two problems for Path #3
  High latency due to additionally passes hardware units
  Bandwidth interference to the others
RDMA of path #3 overuses the PCIe bandwidth
Client
NIC
PCIe1
SoC
PCIe0
Host
…
Case study: file replication in LineFS [SOSP’21]
PCIe 1 & 2 bandwidth
Bi-directional: 256Gbps
Data passes PCIe1 twice
1. NIC  SoC
2. SoC  NIC
Path#2 + Path#3
Peak at 128Gbps!
Client
SoC
Host
Client  SoC  Host
Path #2
Path #3
200Gbps
256Gbps
Notes: From the more zoomed in graph, let's see what's happens. Under path 3, a single piece of data will pass the same PCIe link twice. This may seems not be a problem if the PCIe bandwidth is bi-directional. However, the SoC may concurrently issuing path 2 requests on the same link, so the performance interference happen and we can only achieve half of the PCIe link. (click)
On our evaluated NIC, it is 128Gbps, which is lower than the 200Gbps supported by the NIC.

## Slide 161: Finding 4. Path #3 has trade-offs
DMA: another alternative for path #3
  Unlike RDMA, the SoC has a DMA engine for path #3 (i.e., DOCA DMA)
  DMA bypasses PCIe for communication between SoC and host
Path #3 (RDMA)
Path #3 (DMA)
Chart: 
| READ | WRITE
RDMA | 3.3 | 2.9
DMA | 2.14 | 1.93
Latency (us)
DMA always
better?
Notes: Is there an alternative to Path 3? (click) Yes, the SoC provides a DMA primitive for communication between the SoC and the host. (click)
Using DMA bypasses the NIC core and its PCIe channels, resulting in lower latency and better PCIe utilization compared to RDMA.
But is DMA always better?

## Slide 162: Finding 4. Path #3 has trade-offs
The engine capabilities of RDMA and DMA is different
  RDMA engine (NIC) is more powerful than DMA engine (SoC)
  So RDMA is faster for transferring small data
Path #3 (RDMA)
Path #3 (DMA)
RDMA is executed by the NIC
DMA is executed
by the SoC
Chart: READ payload (Bytes)
| 16B | 64B | 256B | 1KB | 4KB | 16KB | 64KB
DMA | 10.5 | 10.5 | 10.5 | 6.82 | 3.87 | 1.5 | 0.39
RDMA | 25.7 | 25.7 | 25.7 | 21.6 | 6.14 | 1.56 | 0.39
Thpt (Mreqs/sec)
Client
SoC
Host
READ
WRITE
Primitives evaluated
Notes: The problem of DMA is that it has a lower throughput (click), because it relies on the engines on the SoC for execution. Due to the weak capabilities of the SoC, the DMA engine on the SoC is orders of magnitude slower than the engines on the NIC cores, which are used by RDMA.
This results in a fundamental trade-off between throughput and latency for path 3.

## Slide 163: Key takeaway of the above findings
Each communication path of SmartNIC is not perfect
  Inferior performance or performance anomalies needs to take care
SmartNIC
Network
Path #1: Client → NIC → Host memory
Inferior performance vs. RNIC
Notes: In summary, the key takeaway from our findings are as follows: the communication path of SmartNIC is not faster than its corresponding path in a dumb NIC, a performance tax paid to being smart. Furthermore, each path has performance anomalies that developers need to consider when using SmartNIC.
Regarding path #1, the hardware that supports programmability will make its critical path longer.

## Slide 164: Key takeaway of the above findings
Each communication path of SmartNIC is not perfect
  Inferior performance or performance anomalies needs to take care
Path #1: Client → NIC → Host memory
SmartNIC
Path #2: Client → NIC → SoC memory
Network
Faster access
Anomalies, e.g., more PCIe packets
Notes: For path 2, although it is faster than path 1, it has anomalies such as using more PCIe packets. Note that there are more anomalies revealed in our paper.

## Slide 165: Key takeaway of the above findings
Each communication path of SmartNIC is not perfect
  Inferior performance or performance anomalies needs to take care
SmartNIC
Network
Path #1: Client → NIC → Host memory
Path #2: Client → NIC → SoC memory
Path #3: SoC memory ←→ host memory
RDMA: poor PCIe utilization + high latency
DMA: poor throughput
Notes: For path 3, it is evident that neither RDMA nor DMA paths are perfect for achieving low latency and high throughput.

## Slide 166: Back to our key-value store example
Our characterization explains why naïve KVS on SmartNIC is slow
  SoC has wimpy cores (known)
  Path #3 is slow in terms of latency (RDMA) and throughput (DMA)
NIC cores are under-utilized on the SmartNIC
  Which are much faster than the SoC
Index
Values
Client
RNIC
Server
Host DRAM
RNIC
Index
Get(K)
V
SoC
V
SEND
RECV
Chart: Throughput (Mreqs/sec)
| Throughput: Mops
RDMA-KVS | 53.8
SmartNIC-KVS | 5.1
How to help?
Notes: Back to our previous exmaple,
our analysis shows why offloading a key-value store onto a SmartNIC is slow.
First, the computation power of the SoC is weak for processing key-value requests.
Second, the communication required to read the key-value store content, namely, path 3 is ineferior both in terms of throughput and latency. (click)
A more intriguing question to consider is how
we can improve the acceleration of key-value stores by using smartnics? (click)
We have made one key observation: the powerful NIC cores on the SmartNIC are underutilized, opens new design opportunities.

## Slide 167: Observation: a single path is not optimal, but concurrency can help!
A single alternative does not utilize the full power of SmartNIC
  E.g., Bottlenecked by slow SoC–DMA and SoC in our naïve KVS design
Observation: concurrently utilize the SmartNIC power
  E.g., we can utilize the unused RNIC!
Index
Values
Client
RNIC
Server
Host DRAM
RNIC
Index
Get(K)
V
SoC
V
SEND
RECV
Chart: Throughput (Mreqs/sec)
| Throughput: Mops
RDMA-KVS | 53.8
SmartNIC-KVS | 5.1
SmartNIC-KVS + RDMA | 5.1
RDMA KVS
SmartNIC KVS
SmartNIC KVS
+ RDMA
54M
8M
127M
Notes: More specifically, since a single communication path is unable to fully utilize the SmartNIC, we can take advantage of the unused resources on the SmartNIC to achieve better performance! (click)
For example, after saturating the SmartNIC SoC, we found that the NIC can still handle 127 million RDMA traffic for the key-value store.

## Slide 168: More findings: concurrent path can better utilize SmartNIC
Chart: Number of clients
| 1 | 3 | 5 | 7 | 9 | 11
Path 1 | 50.9 | 142.2 | 176.4 | 176.4 | 176.4 | 172.5
Path 2 | 38.7 | 111.4 | 176.2 | 176.4 | 176.4 | 169.2
Path 1+ 2 | 50.9 | 142.2 | 176.4 | 184.6 | 193.9 | 194.8
WRITE 0B Thpt (Mreqs/sec)
Concurrent usage of Path #1 + Path #2
  Observation: SmartNIC seems to reserve NIC cores for different paths
Path #2
Path #1
Concurrent = some clients issues Path #1 ops, other issues Path #2
Chart: Number of clients
| 1 | 3 | 5 | 7 | 9 | 11
Path 1 | 51.4 | 146.8 | 176.4 | 176.4 | 176.4 | 176.4
Path 2 | 39.4 | 113.3 | 176.4 | 176.4 | 176.4 | 176.4
Path 1+ 2 | 51.4 | 146.8 | 176.4 | 184.6 | 193.8 | 195
READ 0B Thpt (Mreqs/sec)
Notes: Based on our observations, we further characterize the concurrent usage of communication paths of the SmartNIC.
First, if both clients use path #1 and path #2 alone, they would hit a a similar bottleneck. Nevertheless, if we dispatch the clients to different paths, they can typically achieve high throughput. (click) This also applies to RDMA READ and WRITE operations.
We suspect that the NIC internally reserves NIC cores for different paths so a concurrent usage can utilize both of them.

## Slide 169: More findings: concurrent path can better utilize SmartNIC
Concurrent usage of Path #1 + Path #3
  Typically, can achieve a higher bandwidth
But, we should take care of interference !
  RDMA is not a good primitive for path #3
Path #1
Path #3* (DMA)
Path #1
Path #3 (RDMA)
Chart: READ Bandwidth (Gbps)
| Throughput: Mops
path 1 | 191
path 2 | 191
path3 | 204
path 3* | 195
1 + 3 | 235
2+3* | 384
Path 1
Path 2
Path 3
Path 3*
Path 1
+3
Path 1
+3*
Perf. + Bandwidth
Interference
Network limit
PCIe limit
Notes: Moreover, concurrently using the internal and external of SmartNICs, namely, using path 1 and path 3 together achieves a better aggregrated bandwidth even higher than the network (click).
Note that we still need to take care of the network interference. RDMA is not a good choice due to the competition on the NIC core and NIC DMA for path 3.

## Slide 170: A guideline on building systems with SnartNIC
Recap the key takeaways from our characterization
  Single path: Inferior performance or performance anomalies
  Concurrent paths: better performance
Our suggested guideline when given a user networked request (e.g., KVS get())
A#1
1. Derive alternatives
Request
A#2
…
…
1.1 Optimize
Opt. A#1
Opt. A#2
With the help of our characterization
2. Evaluate + Rank
A1 A2 A3
3. Select + Combine
SmartNIC
A#2
A#1
Notes: That's the all characterization of our study. Based on it, we suggest utilize the SmartNIC as follows (click).
First, we need to derive different alternatives to implement a given user networked request. (click)
Afterward, we need to optimize each path with the help of our performance characterization. (click)
Then, evaluate and rank each alternative based on system requirements, e.g., latency and throughput. (click)
Finally, we greedyly combine different alternatives until the hardware resources of SmartNIC are saturated.

## Slide 171: Distributed key-value storage Get() revisit
System requirements
  Low host CPU usage, low latency & high throughput
  Low host CPU utilization
1 + 2. Design alternatives (A1—A5) & optimize! :
Client
RNIC
Server
Host DRAM
RNIC
SoC
READ
READ
A1
READ
A2
SEND
RECV
SEND
RECV
READ
A3
READ
READ
A4
READ
READ
+ Index cache
+ value cache
A5
SEND/RECV
Notes: Let's make a final revisit to our key-value store case.
The system requirement is low host CPU usage, low latency and high throughput.
We can see that SmartNIC enables many alternatives for a key-value store.
We won't talk about them in details due to the time constraints.

## Slide 172: Evaluate different alternatives: throughput
The goal: low latency (when there is not so much client)
Client
RNIC
Server
Host DRAM
RNIC
SoC
READ
READ
A1
READ
A2
SEND
RECV
SEND
RECV
READ
A3
READ
READ
A4
READ
READ
A5
SEND/RECV
Chart: 
| Throughput: Mops
RDMA-KVS | 6.9
Chart: 
| Throughput: Mops
RDMA-KVS | 9.8
Chart: 
| Throughput: Mops
RDMA-KVS | 7.5
Chart: 
| Throughput: Mops
RDMA-KVS | 5.9
Chart: 
| Throughput: Mops
RDMA-KVS | 5.2
 | 4.6
Latency
(us)
Offload KVS request on the SoC w/ caching has the lowerst latency
Notes: Based on our guideline, we next rank each alternative with evaluations.
The lowest latency is achieved when all the keys and values are cached on the SoC because we can use one RTT to retrieve it with the help of offloading.

## Slide 173: Evaluate different alternatives: throughput
The goal: high throughput (for a single SmartNIC-powered key-value store)
Client
RNIC
Server
Host DRAM
RNIC
SoC
READ
READ
A1
READ
A2
SEND
RECV
SEND
RECV
READ
A3
READ
READ
A4
READ
READ
A5
SEND/RECV
Chart: 
| Throughput: Mops
RDMA-KVS | 43
Chart: 
| Throughput: Mops
RDMA-KVS | 5
Chart: 
| Throughput: Mops
RDMA-KVS | 7.5
Chart: 
| Throughput: Mops
RDMA-KVS | 58.3
Chart: 
| Throughput: Mops
RDMA-KVS | 70
 | 18
Peak Thpt (Mr/ssec)
Notes: On the other hand, the highest throughput is achieved when using RDMA to access the cached key-value store entries on the SoC, mainly thanks to the efficiency of path #2 RDMA.

## Slide 174: Rank, select and then combine
None of the approaches achieve both low latency & high throughput
  A5(SEND/RECV) has the lowest latency, while A5(RDMA) has the highest throughput
  Note that A5 is not always possible due to memory constraint of SoC
Whenever possible, choose A5 (SEND/RECV) for the lowest latency
  If the SoC has been saturated, switch to A4 & A5 (RDMA)
Evaluation setup: YCSB-C 100% Get( )
Chart: Throughput (Mreqs/sec)
| 0.19 | 0.55000000000000004 | 1.07 | 46.8 | 48.4 | 49.7
RDMA-KVS | 5.4 | 5.55 | 5.58 | 26 | 36 | 70
SmartNIC-KVS (opt) | 4 | 4.2 | 4.5 | 24 | 26 | 31
Latency (us)
Combine A4 + A5
Notes: Based on our rank, we choose A5 for our key-value store whenever possible, and switch to A4,the second best alternative if the value is not cached. Our results show much performance gain compared to a pure RDMA-KVS.